## Slide 1: Tympan Rev A/C Hardware
Line-In / Mic Jack
Headphone Jack
USB to
Program/Recharge
On-Board Mic
Power
Switch
User Pot
(Volume)
Bluetooth
Classic
On-Board Mic
User
LEDs
Li-Po Battery on Back

## Slide 2: Tympan Rev E, Goals
Goals:
  Primary Goal: Smaller
  Secondary Goals: Lower cost, more attractive, BLE, better microphones
Approach:
  Integrate Teensy into Tympan Board, Swap BT Module, Shrink PCB Size, Possibly Change Mics
  Unknowns: Which BLE Module, Which Mics

## Slide 3: Tympan Rev E Ideas
Li-Ion Battery: (add extra room for wires)
Adafruit: 500 mA-hr: 29 x 36 x 4.76 mm
Sparkfun: 400 mA-hr: 26.5 x 36.9 x 5 mm
Li-Ion Battery: (add extra room for wires)
Adafruit: 500 mA-hr: 1.15 x 1.4 x 0.19”
Sparkfun: 400 mA-hr: 1.06 x 1.48 x 0.2”
battery

## Slide 4: Tympan Rev E Ideas
Li-Ion Battery: (add extra room for wires)
Adafruit: 500 mA-hr: 29 x 36 x 4.76 mm
Sparkfun: 400 mA-hr: 26.5 x 36.9 x 5 mm
Li-Ion Battery: (add extra room for wires)
Adafruit: 500 mA-hr: 1.15 x 1.4 x 0.19”
Sparkfun: 400 mA-hr: 1.06 x 1.48 x 0.2”
battery
Top
Top

## Slide 6: Hardware Specs
Processor
  NXP MK66F (ARM Cortex M4F Core)
  180 MHz with Floating-Point Unit
Analog-Digital
  Texas Instruments TLV320AIC3106, stereo ADC and DAC
  32/24/20/16-bit configurable (93 dB SNR)
  Low-noise, software-controllable gain on inputs
  Software-controllable microphone bias
  Software-controllable headphone amplifier
Data Interfaces
  USB Serial, USB Audio, USB HID
  Bluetooth Classic
  SD Card
  Digital microphone port
Power
  Draws about 100 mA @ 3.7V.
  Power from USB or Li-Po Battery
  On-board recharging from USB (with indicators)
Programming
  Reprogram via USB. Program in C/C++.
  Free, open-source toolchain
User Interaction
  Potentiometer, LEDs, Bluetooth